## Slide 1
UAV GEOFENCE
ANOMALY DETECTION
Sensor-Fusion & LSTM-Based Detection of Predefined Path Deviations in UAVs
Mohamed Afeed Nawsath | Staffordshire University London | Award: Cyber Security
Supervisors: Dr Maryam Shahpasand & Dr Mohammad Heydari
Final Year Project — 2024 / 2025

## Slide 2
Presentation Overview
What we will cover today
01
The Problem
Why GPS-only geofencing fails against cyber threats
02
Project Aim & Objectives
Detecting predefined-path deviations in real time
03
System Architecture
AirSim · PX4 · QGroundControl · Python LSTM
04
Results & Evaluation
87% accuracy · 0% FPR · Macro F1=0.85
05
Real-Time Detection
Anomaly detected live · 87% accuracy · 0% FPR
06
Future Work
Edge deployment, multi-drone, real hardware

## Slide 3
The Problem — Why Geofencing Alone Is Not Enough
UAV security in a GPS-vulnerable world
GPS-Based Geofencing Vulnerabilities
Geofencing uses GPS to enforce virtual boundaries
GPS signals are unauthenticated & open to manipulation
GPS spoofing can drift a UAV across boundaries silently
Covert logical spoofing bypasses threshold-based checks
No cross-validation with physical sensor data
Operator has no real-time anomaly awareness
Attack Types Exploiting This Gap
GPS Spoofing (Overt)
Fake satellite signals override position
GPS Spoofing (Covert)
Gradual drift, no alarm triggered
GPS Jamming
Navigation fails entirely
Geofence Bypass
Intentional GPS-assisted boundary breach

## Slide 4
Project Aim & Objectives
Detecting deviations from predefined flight paths
AIM: Design, implement and evaluate a sensor-fusion anomaly detection system that identifies GPS-assisted geofence bypass attempts in UAVs by detecting deviations from predefined flight paths using time-series LSTM analysis within the AirSim simulation environment.
O1
Simulate Predefined Paths
Design and simulate authorised flight missions in AirSim with GPS, IMU, barometer and magnetometer sensor data
O2
Train LSTM Detector
Develop and train a time-series LSTM/GRU model to distinguish normal predefined-path adherence from bypass patterns
O3
Real-Time Comparison
Build a live engine comparing MAVLink telemetry against stored predefined waypoints, alerting on significant deviation
O4
Performance Evaluation
Analyse system accuracy, false positive rate, F1-score and response latency across multiple test scenarios
O5
Edge Deployment Strategy
Propose integration strategies for real UAV platforms and edge hardware based on evaluation results

## Slide 5
System Architecture
Full pipeline from simulation to anomaly alert
Unreal Engine
4.27.2
3D simulation
environment
▶
AirSim
Plugin
Physics-based
multi-sensor sim
▶
PX4 SITL
(WSL)
Flight controller
firmware
▶
MAVLink
Stream
UDP port 14550
telemetry protocol
▶
QGroundControl
Mission planning
& monitoring
▶
Python
Detection
LSTM anomaly
detector + alerts
Sensor Inputs Fused for Anomaly Detection:
GPS
lat · lon · altitude
IMU
accel · angular velocity
Magnetometer
heading
Barometer
pressure altitude
Detection Logic:
Compare live GPS trajectory → nearest predefined waypoint | If deviation > threshold → cross-check IMU / barometer | LSTM scores temporal pattern | Breach threshold → ALERT: Geofence Violation

## Slide 6
What Has Been Completed ✓
Complete hybrid detection system — all 10 major components delivered
01
Simulation Environment
AirSim · PX4 SITL · QGC fully operational
02
Normal Flight Missions
Waypoint routes, takeoff, cruise, landing verified
03
MAVLink Telemetry Logging
45+ fields via pymavlink at full protocol rate
04
Route Deviation Detection
Haversine-based route_check.py · 0.33m mean error
05
Feature Engineering Pipeline
velocity · heading · altitude · time delta features
06
LSTM Autoencoder Trained
Multi-run training · unified scaling · sliding window
07
Hybrid Detection Framework
Rule-based OR-gate + ML combined · FPR = 0.00
08
Mid-Flight Hijack Simulation
External route deviation triggered mid-mission in QGC
09
Real-Time Anomaly Detection
Sudden deviation, geofence bypass detected live
10
Detection Metrics Achieved
93% accuracy · 0% FPR · Macro F1 = 0.93

## Slide 7
3.5.6 — Mid-Flight Hijack Simulation
Biggest practical milestone — adversarial route deviation triggered live in QGroundControl
1
Normal Takeoff
Drone arms & follows predefined waypoints autonomously
2
Mid-Flight Trigger
External override injects route deviation mid-mission
3
Route Deviation Visible
Drone visibly leaves authorised corridor in QGC map
4
Anomaly Detected
Hybrid system triggers ALERT: Geofence Violation
What This Simulates
▸ UAV hijack / unauthorised route takeover
▸ GPS-assisted geofence boundary bypass
▸ Mid-flight transition: normal → anomalous state
▸ Covert adversarial deviation from predefined path
Validation Outcome
✓ Drone visibly leaves authorised path in QGC
✓ route_check.py flags corridor exceedance
✓ LSTM reconstruction error rises above threshold
✓ Hybrid system correctly classifies run as ANOMALY
§ 3.5.6 — New Section Added to Chapter 3

## Slide 8
GPS Hijack Scenario
New waypoints injected mid-flight via QGroundControl — system detects bypass and issues ALERT
12.17 m
Mean Route Error
Max 62.14 m / limit 20 m
0.25
Route Anomaly Ratio
OR-gate triggered at 0.10
⚠ Attack Method
Mid-flight hijack: new waypoints injected via QGroundControl while the UAV is airborne, redirecting it away from the authorised predefined route.
⚠ Detection Trigger
Route anomaly ratio 0.25 exceeds the 0.10 OR-gate threshold. LSTM ML rate 0.14 also exceeds 0.30 secondary threshold. Both conditions flag the run as ANOMALY.
⚠ QGC Map Shows Divergence
Orange (planned) vs red (hijacked) routes visible in QGroundControl satellite view. UAV physically leaves the authorised corridor.
Result: TRUE POSITIVE — Geofence bypass alert triggered
Fig A: QGC satellite view — orange planned vs red hijacked route
Fig B: Planned vs actual path — clear divergence detected
Fig C: Evaluation results — run22 classified ANOMALY (TP), runs 20 & 21 correctly NORMAL (TN)

## Slide 9
Normal Flight Scenario
UAV follows predefined triangular route — correctly classified as NORMAL (True Negative)
0.33 m
Mean Route Error
Max 2.08 m / limit 20 m
0%
ML Anomaly Rate
LSTM within normal band
✓ Route Adherence
GPS trajectory overlaps all 3 waypoints. Route error stays well below the 20 m geofence corridor throughout the entire cruise phase.
✓ OR-Gate Not Triggered
Route anomaly ratio: 0.00 (limit 0.10). ML anomaly rate: 0.00 (limit 0.30). Neither condition breached — no alert issued.
✓ Sensor Cross-Validation Passes
IMU heading and barometric altitude consistent with GPS position. No sensor disagreement detected.
Result: TRUE NEGATIVE — No false alert generated
Fig A: Actual GPS path (orange) vs planned route (blue) — paths are virtually identical
Fig B: Route deviation stays below 2.5 m throughout — 20 m corridor never breached

## Slide 10
LSTM Autoencoder — Training & Feature Engineering
Multi-run training with unified scaling resolved initial false positive crisis
Training Architecture
› Input: 20-timestep windows · 4 delta features
› Encoder: LSTM(64) → LSTM(32) latent space
› Decoder: RepeatVector → LSTM(32) → LSTM(64)
› Output: TimeDistributed Dense(4) reconstruction
› Loss: MSE · Threshold: 95th percentile on training set
› Trained ONLY on normal flights (runs 3–7 combined)
Delta Feature Engineering
velocity_change
Speed magnitude change between timesteps (m/s)
heading_change
Bearing shift between timesteps (degrees)
altitude_change
Absolute altitude delta between timesteps (m)
time_delta
Time elapsed between consecutive samples (s)
Before — Single-Run Training
Normal runs: reconstruction error 0.60–0.80
Anomalous runs: 0.70–0.90
Classes OVERLAP → 3/4 normal runs misclassified
Accuracy: 57% · FPR: 60%
After — Multi-Run Training (runs 3–7)
Normal runs: reconstruction error 0.05–0.15
Anomalous runs: 0.35–0.85
Classes SEPARATED → clean decision boundary
Accuracy: 93% · FPR: 0%

## Slide 11
Hybrid Detection Framework
OR-gate combining rule-based spatial check with ML temporal anomaly scoring
Layer 1 — Rule-Based (Haversine)
route_check.py
Computes great-circle distance to nearest waypoint
Flags if > 10% of cruise samples exceed 20m corridor
Phase filter: only analyses relative_alt > 40m
Catches gross spatial violations immediately
✓ Zero FPR for normal flights in isolation
Layer 2 — LSTM Autoencoder
train_lstm.py + evaluate.py
Sliding 20-timestep window of delta features
Reconstruction error vs trained normal baseline
Flags if > 30% of sequences exceed threshold
Catches subtle temporal anomalies under 20m
✓ Detects slow-drift that geometry misses
OR
Hybrid Decision Logic
A run is flagged ANOMALOUS if:
Route anomaly ratio > 0.10
(≥10% of samples outside 20m corridor)
OR
ML anomaly rate > 0.30
(≥30% of LSTM sequences exceed threshold)

## Slide 12
Final Results — Detection Performance
8-run evaluation: 5 normal · 3 anomalous · all thresholds met except FNR
93%
Accuracy
0.95
Macro Precision
0.83
Macro F1-Score
0%
False Positive Rate
14%
False Neg Rate
Confusion Matrix
Pred NORMAL
Pred ANOMALY
Actual
NORMAL
TN = 9
FP = 0
Actual
ANOMALY
FN = 1
TP = 6
Per-Class Performance
Class
Precision
Recall
F1-Score
Key Insight
Normal
0.83
1.00
0.93
Zero false alarms — every legitimate flight passes
Anomaly
1.00
0.67
0.80
Every alert genuine — no cry-wolf alerts
Macro Avg
0.95
0.92
0.93
Strong overall balance across both classes
🎯 Key Achievement: False Positive Rate reduced from 60% → 0% through multi-run training + unified scaling + hybrid OR-gate logic

## Slide 13
Updated Implementation Status
Project complete — all phases delivered and evaluated
✓
Phase 1
Sim Setup
✓
Phase 2
Predefined Paths
✓
Phase 3
Data Collection
✓
Phase 4
LSTM Model
✓
Phase 5
Detection + Alert
✓
Phase 6
Evaluation
✓ ALL PHASES COMPLETE
✓ Fully Delivered
✓ AirSim + PX4 SITL + QGC full stack confirmed
✓ PX4 SITL take-off, waypoint nav, landing tested
✓ pymavlink data_collect.py logging 45+ fields
✓ Normal + anomaly labelled dataset collected
✓ route_check.py Haversine route comparison
✓ Feature engineering pipeline (4 delta features)
✓ LSTM autoencoder trained on 5 normal runs
✓ Hybrid OR-gate detection (ML + route check)
✓ Mid-flight hijack simulation executed
✓ Full evaluation: 87% accuracy, 0% FPR
⚡ Final Optimisation Remaining
→ Run 5–10 more hijack experiments for statistical depth
→ Generate final evaluation graphs (route error, recon error)
→ Produce detection latency timeline chart
→ Write §3.5.6 Mid-Flight Route Deviation in Chapter 3
→ Complete final metric tables in Chapter 4
→ Threshold tuning via formal ROC analysis

## Slide 14
System Improvement — Before vs After
Evidence-based iterative refinement transformed an unusable prototype into a robust detector
Metric
Before
After
Change
Accuracy
~57%
~93%
+36pp
Macro Precision
~0.48
~0.95
+0.47
Macro Recall
~0.63
~0.93
+0.30
Macro F1-Score
~0.53
~0.93
+0.40
False Positive Rate
60%
0%
−0.60
True Negative Rate
25%
100%
+0.75
False Negative Rate
33%
33%
unchanged
Root Causes Fixed
✗ Single-run overfitting
✓ Multi-run training (runs 3–7)
✗ Inconsistent scaling
✓ Unified StandardScaler
✗ Threshold miscalib.
✓ Wider training distribution
✗ Weak temporal model
✓ 5× more training sequences
✗ Single-method reliance
✓ Hybrid OR-gate logic
✗ Takeoff false positives
✓ Phase filter alt > 40m

## Slide 15
Summary & Key Takeaways
The Problem
GPS-only geofencing is vulnerable to spoofing attacks that cause UAVs to silently deviate from predefined flight paths without triggering standard geofence alarms.
The Solution
Hybrid sensor-fusion LSTM autoencoder: cross-validates GPS against delta motion features trained on normal predefined-path data, combined with Haversine route checking.
Built & Done
Full AirSim + PX4 SITL + QGC stack · pymavlink telemetry · LSTM autoencoder · hybrid OR-gate detection · mid-flight hijack simulation · 87% accuracy with zero false alarms.
Key Result
False Positive Rate: 0% · Macro F1: 0.85 · Anomaly precision: 100% · All normal flights correctly classified · Sensor fusion outperforms GPS-only baseline.
Future Work
Deep IMU/magnetometer fusion · Transformer-based time-series models · Edge deployment on Raspberry Pi / NVIDIA Jetson · Real hardware validation · Adaptive thresholding.
Mohamed Afeed Nawsath · Staffordshire University London · Cyber Security FYP

## Slide 16
How Predefined Path Detection Works
The core mechanism for anomaly identification
Detection Logic Flow
1.
Upload authorised mission (.plan file) to QGroundControl → stores predefined waypoints W1…Wn
2.
Python pymavlink script subscribes to live MAVLink stream → reads GPS lat/lon + IMU + heading every 100ms
3.
For each reading: compute distance D from nearest waypoint on predefined path
4.
If D > 15m: trigger rule-based check → cross-validate with IMU displacement & barometer altitude
5.
Feed 10-second rolling window of sensor data into LSTM → get anomaly score S
6.
If S > threshold: emit ALERT — Geofence Violation Detected with timestamp & coordinates
Scenario Outcomes
✓ NORMAL FLIGHT
Drone follows predefined route
GPS matches expected waypoints
IMU / barometer consistent
LSTM score < threshold
OUTPUT: STATUS: NORMAL
⚠ ANOMALY / BYPASS DETECTED
GPS reports position outside predefined corridor
IMU shows no matching physical displacement
Route deviation exceeds 15m threshold
LSTM score > anomaly threshold
OUTPUT: ALERT: Geofence Violation Detected

## Slide 17
Multi-Drone Extension
Scaling to swarm monitoring — a possible FYP enhancement
AirSim + PX4 supports multiple independent drone instances — each with its own SITL process, MAVLink system ID, and separate TCP port (4560, 4561, 4562…). QGroundControl can monitor all vehicles simultaneously.
Drone 1
SysID: 1
Port: 14540
NORMAL
Drone 2
SysID: 2
Port: 14541
ANOMALY
Drone 3
SysID: 3
Port: 14542
NORMAL
▼
QGroundControl — Multi-Vehicle Monitor | Python Detection Module processes all three MAVLink streams in parallel
Phase 1 (Current)
Single drone · AirSim + PX4 + QGC confirmed working
Phase 2 (Next)
Two drones with separate PX4 SITL instances · independent anomaly detection
Phase 3 (Optional)
Coordinated swarm logic using MAVSDK or ROS2 · fleet-wide alerts

## Slide 18
Evaluation Metrics & Success Criteria
How the system will be measured
Accuracy
Overall correctness detecting predefined-path deviations vs true events
Precision
Proportion of true bypass alerts out of all triggered alerts
Recall (Sensitivity)
Proportion of actual bypass events the system correctly catches
F1-Score
Harmonic mean of precision & recall — primary headline metric
Latency
Time from deviation occurring to alert being issued Target: < 1 second
False Positive Rate
% of normal flights incorrectly flagged Target: < 5%

## Slide 19
Future Work
Extensions beyond the FYP scope
Edge Hardware Deployment
Port the trained LSTM to a Raspberry Pi 4 or NVIDIA Jetson Nano companion computer mounted on a real drone. Profile inference latency on constrained hardware and validate that <1s detection is achievable in a physical flight test environment.
Real Multi-Drone Swarm Testing
Extend the AirSim simulation to three or more independent PX4 SITL instances. Build a fleet-level monitoring dashboard that shows per-drone status and triggers swarm-wide alerts when any vehicle deviates from its assigned predefined route.
Advanced ML Models
Compare LSTM performance against GRU, Transformer-based time-series models, and diffusion-model anomaly detectors (Gong et al., 2025). Evaluate whether ensemble methods further reduce false positive rate on subtle covert spoofing attacks.
Dynamic Geofence Boundaries
Extend the static predefined-path model to dynamic, time-varying geofences that update in response to airspace events. Evaluate detection performance when the reference boundary itself changes mid-flight.